# Description  of  50 ml   LUER – LOCK  syringes

Three-part, single use syringes of 50 ml with the conical fitting LUER-LOCK are sterile, non-pyrogenic and non-toxic. They consist of three pieces: barrel, plunger and rubber piston. Barrel and plunger are made of transparent plastic (polypropylene) and the rubber piston is made of a special, medical quality rubber (no latex).

The syringes are mainly created and used by the professional medical staff for the infusion pumps.

The standard conical fitting LUER is surrounded by screw and meets the requirements of the standard ISO 594-2 (EN 1707) and it is in a central part of the bottom of the barrel.

The syringes are sterilized with ETO sterilization process. The process has been validated according the present, obligatory standard, which is confirmed by suitable certificates.

The syringes of 50 ml have clear and readable scale, marked every 1,0 ml. The figures are printed on the scale every 10 ml. The accuracy of the scale is guaranteed. The scale is extended up to 60 ml.

The rubber piston is very tight to the internal flank of the barrel.

The unit package is created as blister-pack formed of welded paper and film. It protects the sterile syringe from the contamination during the whole life time of the product.

The transport box contains 220 pieces of the syringes.

On each unit package and transport box  there is a readable and clear information, which allows fast and easy identification of the syringes, its LOT number and expire date.

The life – time of the 50 ml LUER syringe is 3 years.

The REF Number:   ST.50.02